Multi-Scale Tissue Mechanics Modeling Issues

| Scale | Modeling Need | Method/Type | Software | Issues | Possible Shared Items |
| --- | --- | --- | --- | --- | --- |
| Organ Systems | Determination of organ level mechanical loading Musculoskeletal model sensitivity studies Neuromusculoskeletal model optimization studies (Muscle activation patterns) 1 | Multi- body musculoskeletal model (lumped parameter) | MSC.ADAMS SIMM/Dynamics Pipeline/SDFAST | Difficult to represent soft tissues in non-FE models Kinematic/kinetic model of joint should be adequate to represent organ level loading , e.g. is it possible to use knee BCs and loading obtained using a hinge description in a follow-up complex finite element model of the knee? | Simulation Results Tissue loading, ligament strain, muscle activation patterns Solution algorithms |
| Organ | Need for computationally efficient models that capture dynamic tissue behavior | Artificial Neural Network Support Vector Machines Surrogate modeling based on adaptive sampling and local interpolation | MATLAB Neural Network Toolbox SPIDER (a free machine learning toolbox for Matlab) | Space and time complexities Stability Generalization | Modeling Technique Journal Article ANN models that capture desired responses from computationally intensive techniques Modular application programming interface IDE compatibility Solution database of complex models |
| Organ | Convert MR/CT images to 3-D geometries | N/A | Slicer Mimics Materialise Volsuite | Thresholding techniques typically do not work well on musculoskeletal tissues converted geometries typically need smoothing integrity of tissue geometries/thickness maintained? | Tissue Geometries STL files Patient Specific IGS files |
| Tissue | Meshed tissue geometries | N/A | Cubit Patran TrueGrid | Irregular surfaces difficult to mesh particularly using hexahedral elements STL format not optimal for meshing Conversion of STL to NURB surfaces? Automated generation of tetrahedral meshes is possible but those may not be suitable for nonlinear simulations Are meshfree methods a solution? | FE meshed geometries of tissues Parametric meshing scripts |
| Tissue | Accurate representation of Non-linear, Non-homogenous, Viscoelastic tissues | Finite - Element Inverse finite element method | ABAQUS | FE method is computationally intensive for dynamic simulations meshing contacts need for accurate constitutive equations therefore complete experimental data sets material heterogeneity | Modeling Technique Journal Article Constitutive equations Experimental data to develop constitutive models |
| Multi-cell | Develop constitutive equations of tissue | Pseudo – Bond | Custom | Material parameter estimation | Modeling Technique Journal Articles Constitutive equations of tissues Platform specific ? |
|  |  | Boundary Condition coupling |  |  | Modeling algorithms that couple 1D and 3D lung models |

Guess, Lin, Bischoff, Erdemir,

1 For a review of current methods, see "Erdemir, A., McLean, S., Herzog, W. and van den Bogert, A. J. (2007) Model-based estimation of muscle forces exerted during movements, Clinical Biomechanics, 22, 131-154". I'll be happy to upload the article to SimTk site. I wonder if we violate any publisher copyright rules if we upload original articles though.