## Slide 1: Determination of Deformation from Medical Imaging
Alexander I. Veress
Research Assistant Professor
Department of Mechanical Engineering
University of Washington
NSR class August 29, 2008

## Slide 2: Motivation
Physician use qualitative measures such as wall motion and wall thickening to estimate cardiac wall health.
Deformation is a direct measure of cardiac contraction and dilation which can provide valuable information on cardiac function and viability of diseased tissue.
Deformation and wall strain may be determined from tagged MRI.

## Slide 3: Deformation Determined by Tagged MRI
Planes of myocardial tissue are marked or “tagged” using spatially selective radiofrequency pulses that appear as dark lines in the MR images.
The tags move with the underlying tissue and can be tracked over the heart cycle using gated images.
Tagged image strain analysis has a course spatial resolution (6 mm tag spacing optimal [1])
Not used clinically probably due to time, two or three orthogonal acquisitions are necessary, and expense.
[1] Atalaret al. (1994), IEEE Trans Med Imag 13(1), pp. 152-160

## Slide 4: Problem
Are there regional differences in wall deformation (strain) between normal and hypertensive rats over the animals two year life spans.
Gated PET image data was gathered to determine metabolic differences as well as to be used to determine deformation.

## Slide 5
MicroPET II
normotensive
hypertensive
Problem: PET Imaging was used to monitor disease progression in normal and SHR rats over lifespan of animals
Diastolic deformation was determined from images acquired over life spans of normotensive and spontaneously hypertensive rats (SHR).
Images acquired at UC Davis
F-18 Fluoro-2-Deoxyglucose
(18FDG)

## Slide 6: Available Information
Subject-specific geometry from PET images
Appropriate material model and properties
Fiber structure
    Relied on literature values
Loading and boundary conditions
  Intraventricular pressures not available

## Slide 7: Measurement of Deformation using Hyperelastic Warping
What deformation map will make the template image deform to look like the target image.
Template Image
end-systole
Target Image
end-diastole
(X)
Deformation map
Systolic relaxation
diastolic filling.

## Slide 8: Data Flow
Finite element model is a descritization of the image in addition to being
a representation of the LV.
Notes: In hyperelastic warping the image data, assumed material properties, and boundary conditions (if known) are inputs to the non-linear Warping FE model. The deformation map and the stress and strain can be determined from the image data sets.

## Slide 9: Hyperelastic Warping - Based on Computational Solid Mechanics
Energy functional contains elastic energy and image-based energy:
 is the deformation map
C is the right deformation tensor
T is template image intensity
S is target image intensity
 is a penalty number
hyperelastic energy
image-based energy
Notes: hyperelastic strain energy term found in standard FE analysis. This term is an image based energy term that is simply the point-wise difference in pixel intensities (second Eq). psi is the deformation map, C is the right deformation tensor, T is template image intensity, S is target image intensity, lambda is a penalty number which scales the image force.

## Slide 10: Difference Image Determines Forces
Template Image Uniaxial loading Target Image
Difference Image

## Slide 11: Development of Warping Force
Template
Image
Target image
with Template
mesh
superimposed
Registration of
images decreases
Warping forces
With alignment,
pointwise
difference
in intensities
and their
gradients are
minimized
Notes: With alignment, pointwise difference in intensities and their gradients are minimized over the domain of the finite element mesh.

## Slide 12: Hypothesis
Mechanical properties of the myocardium change as a function of hypertension, and these changes in material properties can be seen in the altered diastolic function of the LV over the course of the life of the subject.

## Slide 13
Manually segment (A) from imaging data.
Segmented curves define surfaces
FE mesh created from surface definitions (B) using TrueGrid pre-processor (XYZ Scientific Applications, Inc).
Typical model has 1000-7000 nodes and 500-5000 hexahedral, isoparametric elements.
Models analyzed using Nike3D FEM package (non-linear, large deformation).
Finite Element Mechanical Model Creation
A
B
epicardium
endocardium
Notes: The deformation the heart undergoes is documented in the standard cardiac images that are routinely used in diagnosis of cardiac function. Hyperelastic warping takes a descritized representation of the template image and deforms it until it registers with the target image.

## Slide 14: Ejection Fraction
2003
2004
Ejection Fraction does not
show the effects of the increased
pressure within the LV for the
SHR subjects compared with the
normal control.
Hypothesis: A direct measure
of deformation such as strain
would be more sensitive changes
in cardiac function due to
Hypertension.

## Slide 15: Results: SHR Temporal Study
2 year study of 2 SHR rats and a normotensive control (WKY).
Little or no 18FDG uptake in second year of life of control.
Lateral wall or anterior/lateral wall shows the largest deformation.

## Slide 16
SUMMARY
There appears to be little difference in EF between SHR and WKY.
Differences in diastolic deformation between SHR and WKY appear in the second year of life.
Lateral and anterior/lateral wall experiences greatest deformation during diastole resulting from the greater pressure load.

## Slide 17
Fatty acid
Normal:
Disease
Major Fuels
for the Myocardium
Stress:
Glucose

## Slide 18: Limitations of Warping
Can only be used to analyze passive mechanics such as diastolic relaxation and filling.
Analysis of systolic contraction leads to element inversion and incomplete analysis of the problem (poor image registration).

## Slide 19
Pinhole SPECT
90 1sec projections (128×128) per rotation
36 rotations (1hr)
Protocol
Injected 5mCi 123I-BMIPP
(radio labeled fatty acid analog)
80×80×80
0.85 mm
Reconstruction
Acquisition

## Slide 20
WKY (no mark)
SHR (no mark)
WKY (blue)
SHR (red)
123I-BMIPP
Half a year
old.
SHR shows similar fatty acid uptake as WKY normals.

## Slide 21
WKY (no mark)
SHR (no mark)
WKY (blue)
SHR (red)
123I-BMIPP
Over a year old
SHR Shows decreased fatty acid uptake.

## Slide 22
Heart Structure
The forward model of the left ventricle (LV)
Hyperelastic Warping to determine the deformation of the LV
Active Contraction Warping

## Slide 23: Active Contraction Warping
An active contraction component has been added to Warping in order to analyze systolic behavior.
Initially, literature values of active contraction stress were used.
Active contraction was coupled to amount of image mismatch between descritized template and target image.

## Slide 24: Coupling of Active Contraction with Image Mismatch
Ct governs shape of activation curve.
Previously, literature values were used for Ct.
We have coupled this term to the average image intensity difference in the left ventricle wall.  penalty parameter used to enforce the contraction.
Produces uniform contraction across the LV wall.

## Slide 25: Comparison with tagged-MRI Images
Deformations were determined of a single mid-ventricular slice from a normal human subject imaged using PET and analyzed with augmented Warping.
Compared with tagged MRI images from the same patient.
end-systolic
target
PET images used in analysis
end-diastolic
template

## Slide 26: Comparison with tagged-MRI Images
Deformations were determined of a single mid-ventricular slice from a normal human subject imaged using PET and analyzed with augmented Warping.
Compared with tagged MRI images from the same patient.
end-systolic
target
PET images used in analysis
end-diastolic
template

## Slide 27: Comparison with tagged MRI images
Image registration (epi- and endocardial surfaces) using the PET images compared to MRI end-systolic image indicates excellent registration was achieved through analysis of PET images.

## Slide 28: Initial Comparison of Quadrant Circumferential Strain Values
LV split into 8 regions. Initial strain results indicate good agreement
harmonic phase MRI (HARP)

## Slide 29
SUMMARY
Augmented Warping shows promise in the analysis of systolic contraction as demonstrated by analysis of PET patient data.
Entire heart will be analyzed and the deformations will be compared with harmonic phase MRI (HARP) analyzed tagged MRI deformation data.

## Slide 30: Contributors
Investigators
  Grant Gullberg, Lawrence Berkeley Lab
  Jeff Weiss, Bioengineering, U. Utah
  W. Paul Segars, Radiology, Duke University
Development Staff
  Steve Maas, Bioengineering, U. Utah

## Slide 31: Exercises