## Slide 1: Cardiovascular blood flow
Alexander I. Veress1,2
and
Feng Gao2
University of Washington
Mechanical Engineering1
and Department of Bioengineering2
NSR class August 29, 2008

## Slide 2: Outline
Pressures and flows.
Poiseuille Flow.
Pressure-volume-flow relationships in blood vessels.
Dynamics of pulsatile flow.
Pulse wave forms.
Pulse pressure amplification.
Conservation of Mass
Conservation of Momentum
Computational Fluid Dynamics

## Slide 3: Description of Pathology
Supravalvular aortic stenosis is a narrowing of the aorta distal to the aortic valves.

## Slide 4: Supravalvular Aortic Stenosis
It occurs as a localized or a diffuse narrowing of the aorta beyond the superior margin of the sinuses of Valsalva.
It accounts for less than 7% of all fixed forms of congenital LVOT obstructive lesions.

## Slide 5: Pressures and Flows in Steady States
Velocity of Blood Stream
  Q volumetric flow (ml/sec) and A cross-sectional area (mm2)
Changes in cross-sectional area of the same flow will proportionally alter velocity.
or
Q
If Q1 = Q2
1
2

## Slide 6: Static and Dynamic Pressures in steady states flows
Q
Static pressure is the lateral pressure exerted on the wall.
Total pressure is the lateral pressure plus a dynamic pressure or Ptot= Pstat + Pdyn
Detect total pressure.
Detect static pressure.
 is the density of the blood

## Slide 7: Bernoulli’s Equation for Ideal Fluid Flow
The fluid is incompressible.
Pressures and velocities along a streamline.
No friction between the fluid and the wall.
The fluid flow is laminar and steady state.
  Non-steady state flow

## Slide 8: Bernoulli’s Equation Cont.
Non-steady state flow.
 is the flow potential and f(t) is a function resulting from integration (see handout pdf)

## Slide 9: Viscosity and Newtonian Flow
Plate is moving under applied force F and has a contact area of A. The viscosity  is the ratio of shear stress to shear rate.
The shear stress is F/A. The velocity profile u/y is linear so this is a Newtonian liquid.
Note: suspensions such as blood are non-Newtonian.

## Slide 10: Hagen - Poiseuille Flow
  Hagen - Poiseuille flow
    Parabolic velocity profile
    Average velocity
R
Q
L
P1
P2

## Slide 11: Hagen - Poiseuille Flow Cont.
Flow of a Newtonian, laminar flow down a tube which has a flow rate as follows:

## Slide 12: Resistance to Flow
Q
Pi
R
Po

## Slide 13: Resistances in Series
Pi
R1
P2
Q
Po
R2

## Slide 14: Resistances in Parallel
Pi
Po
R1
Q1
R2
Q2
Qtot

## Slide 15: Tubulent vs Laminar Flow
Transition from laminar to turbulent flow occurs for relatively large Reynolds numbers >2000 for blood, e.g. aortic stenosis, bifurations, etc.
where Vm is the mean velocity, D is the characteristic diameter and  is the viscosity.

## Slide 16: Limitations for use of Analytical Equations
Fluid is Non-Newtonian.
Flow reverses with both laminar and turbulent (rotational) flow conditions.

## Slide 17: The Real World: Dynamics of Pulsatile Flow
Pulse pressure in carotid artery.

## Slide 18: Pulse Wave Forms
Adapted from WW Nichols & MF O'Rourke (1998) McDonald's Blood Flow in Arteries: Theoretical, Experimental and Clinical Principles (4th Edition). Edward Arnold, London.
The pulse wave forms for both velocity and pressure change as one travels down the aorta.
These are measurements of a canine subject.
Depending upon where the stenosis is the pulse wave form at the entrance of obstruction will differ.

## Slide 19: Pulse Pressure Amplification
Adapted from WW Nichols & MF O'Rourke (1998) McDonald's Blood Flow in Arteries: Theoretical, Experimental and Clinical Principles (4th Edition). Edward Arnold, London.
The pulse pressure, the difference between systolic and diastolic pressure, increases with distance down the vascular tree.
Canine data shown.

## Slide 20: Pressure Drops along normal portions of the Vascular Tree
Smith JJ and Kampine JP. Circulatory physiology: The essentials. 3rd ed. 1990.
Little loss in pressure in aorta and arteries
Largest pressure drop occurs in arterioles
Pulsatile nature of pressure small in arterioles and nonexistent in capillaries, venules and veins

## Slide 21: Surgical Correction
Increased pressure load causes heart to work harder
  hypertrophic cardiomyopathy
  Heart failure results
Surgical correction is necessary.

## Slide 22
Suppose we have a fluid with local density ρ = ρ (x,y,z,t) and local velocity u=u (x,y,z,t).
Conservation of Mass

## Slide 23
Mass of in
Mass of out
The change of mass in x direction is

## Slide 24
change of mass in y and z direction：
the change of mass is:
The change of density ρ，is

## Slide 25
The mass of change due to the change of density is
we get
For the steady flow, so ，then we get
(3-27)
for incompressible flow, then

## Slide 26: 2. Conservation of Momentum

## Slide 27
According to Newton’s second law of motion, in x direction
We can get
We also can get

## Slide 28
We can write as the following (Euler equation)
Considering the viscosity, we can get the Navier-Stokes equation:

## Slide 29: CFD Modeling
Aorta and cardiovascular diseases
FE Model for FSI (Fluid-Structure Interaction)

## Slide 30: Overall Strategy for FSI
CFD (Computational Fluid Dynamics)
  Solve the fluid velocity and pressure
  Calculate the traction vector at the interface
CSD (Computational Structural Dynamics)
  Apply fluid traction on elastic body
  Calculate displacement and update the surface location
CMD (Computational Mesh Dynamics)
  Use the elastostatic model to determine fluid mesh displacement
  Update the fluid mesh geometry

## Slide 31: Computational Condition
CFD package Fidap 8.7.2 (Fluent Inc. )
Density of fluid: 1050 kg/m3
Viscosity: 0.0035 Pa·s
Poisson coefficient: 0.45 (nearly incompressible material)
Inlet: fixed
Outlet: the out edge of outlet was constrained in the axial direction and permitted to move in the other directions.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 32: Velocity and Pressure -Steady flow
Velocity and pressure are depicted in the longitudinal section of the aortic arch. (velocity agrees with Endo et al. 1996, Shahcheraghi et al. 2002)
Notes: <number>
<footer>
<header>
<date/time>
Blunted ascending reverse

## Slide 33: Wall Deformations -Steady Flow
Deformations of
aorta wall at a=45° (become elliptical)
Changes of the aorta diameter along arch
Displacement of the wall along arch
Notes: <number>
<footer>
<header>
<date/time>
Serious portion elliptical

## Slide 34: Velocity –pulsatile flow
(a) Max Acceleration
(b) Peak Flow
(c) Max Deceleration
(d) Reversed Flow Max)
(a): from the outer to the inner wall (b)(c)(d): from the inner to outer wall (c)(d): clockwise-rotating vortex
Notes: <number>
<footer>
<header>
<date/time>

## Slide 35: Pressure –pulsatile flow
(a) Max Acceleration; (b) Peak Flow; (c) Max Deceleration; (d) Reversed Flow Max
(a)(b) the pressure is maximum at inlet of aorta;
low pressure region is the outlet of aorta.
(c)(d) the relative pressure at inlet of aorta becomes negative value.
The lager acceleration leads to the larger fluid pressure.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 36: Displacement -Pulsatile flow
(a) Max Acceleration; (b) Peak Flow; (c) Max Deceleration; (d) Reversed Flow Max
(a) (b) towards the left side of arch; maximum at the top of arch portion.
(c) reverses towards the right side of arch; (d) The displacement of aorta wall is reduced.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 37: Wall Deformation
In arch radial direction In arch axial direction
The value of deformation in axial direction is very different from that in arch radial direction, so the section of wall could not keep circle.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 38: Further considerations
Material properties and Material Models
Outflow Pressure
External forces induced by surrounding tissue and organs
Realistic geometry
Contraction