## Slide 1: TriSeg CircAdapt Model
Using Matlab to model the heart and circulation
Bart Jardine,
Dept. of Bioengineering, University of Washington
Model authors:
JOOST LUMENS, TAMMO DELHAAS, BORUT KIRN, and THEO ARTS, “Three-Wall Segment (TriSeg) Model Describing Mechanics and Hemodynamics of Ventricular Interaction”, Annals of Biomedical Engineering, Vol. 37, No. 11, November 2009 ( 2009) pp. 2234–2255
Physiome web link (model #0013):
http://www.physiome.org/jsim/models/webmodel/NSR/NON_JSIM_MODELS/CircAdapt_TriSeg_2009/

## Slide 2: TriSeg CircAdapt Model
Model overview:
  Adaptive Lumped model of heart and circulation.
  Simulates heart-beat hemodynamics and mechanical load.
  Model adapts to changes in parameters (due to stenosis, hypertension, exercise, etc..) and can be run to a steady-state.
  Designed to be modular.

## Slide 3: TriSeg CircAdapt Model
Figure 2a: Lumens, et al. 2009

## Slide 4: TriSeg CircAdapt Model
  Heart:
  Heart (ventricular) mechanics incorporate mechanical interactions between the left and right ventricle and interventricular septum in a time dependent fashion (Tri-segment).
  Involves coupling the myofiber mechanics in the three walls to satisfy tensile force equilibrium (Pressure and volume of ventricles change over time due to load adaption).
  R. and L. Atrium mechanics are represented by a simple time dependent relationship between the myofiber length and stress.

## Slide 5: TriSeg CircAdapt Model
Tube: Represents entrance of compliant blood vessel capable of propagating a pressure-flow wave component onto constant flow. (Constant compliance)
Valve: Cross-sectional area depends on flow and transvalvular pressure.
Resistance: Represents systemic and pulmonary microcirculation and connects arterial and venous module.

## Slide 6: CircAdapt Model Description
Figure 2: Arts et al. 2005

## Slide 7: TriSeg CircAdapt Model
Adaption rules:
Heart geometries: Adapts to load through contractility of sarcomeres
Tube: Cross sect area adapts to maintain constant flow.
Resistance (pulmonary peripheral): Mean pressure drop over the pulmonary system is kept constant by changes in resistance after each cardiac cycle.

## Slide 8: Data validation
Original CircAdapt model was validated against fetal heart studies.
Sensitivity analysis of parameters for normal adult.
The tri-segmented heart modified (‘TriSeg Circ Adapt’) model validated against patients w/wo pulmonary hypertension (Pulmonary flow times, RV ejection times, RV isovolumetric contraction/relax times).

## Slide 9: Data validation
Arts et al. 2005

## Slide 10: Next step
Validate against more data (other cardiopulmonary diseases)
Add Lung air gas exchange.
Add blood tissue exchange (capillary) in organs, muscle.
Add explicit baroreceptor modeling.

## Slide 11: References:
Theo Arts, Tammo Delhaas, Peter Bovendeerd, Xander Verbeek, and Frits W. Prinzen., ”Adaptation to mechanical load determines shape and properties of heart and circulation: the CircAdapt model”, Am J Physiol Heart Circ Physiol 288: H1943–H1954, 2005
Lumens J, Delhaas T, Kirn B, Arts T, “Three-Wall Segment (TriSeg) Model Describing Mechanics and Hemodynamics of Ventricular Interaction”, Annals of Biomedical Engineering, Vol. 37, No. 11, November 2009 pp. 2234–2255